## Slide 1: Introduction to 8085 Instructions

## Slide 2: The 8085 Instructions
Since the 8085 is an 8-bit device it can have up to 28
(256) instructions.
  However, the 8085 only uses 246 combinations that represent a total of 74 instructions.
– Most of the instructions have more than one format.
These instructions can be grouped into five different groups:
  Data Transfer Operations
  Arithmetic Operations
  Logic Operations
  Branch Operations
  Machine Control Operations

## Slide 3: Instruction and Data Formats
Each instruction has two parts.
  The first part is the task or operation to be performed.
    This part is called the “opcode” (operation code).
  The second part is the data to be operated on
    Called the “operand”.

## Slide 4: Data Transfer Operations
These operations simply COPY the data from the source to the destination.
MOV, MVI, LDA, and STA
They transfer:
  Data between registers.
  Data Byte to a register or memory location.
  Data between a memory location and a register.
  Data between an I\O Device and the accumulator.
– The data in the source is not changed.

## Slide 5: The LXI instruction
The 8085 provides an instruction to place the 16-bit data into the register pair in one step.
  LXI Rp, <16-bit address> (Load eXtended Immediate)
The instruction LXI B 4000H will place the 16-bit number 4000 into the register pair B, C.
  The upper two digits are placed in the 1st register of the pair and the lower two digits in the 2nd .
40
00
LXI B 40 00H
B
C

## Slide 6: The Memory “Register”
Most of the instructions of the 8085 can use a memory location in place of a register.
  The memory location will become the “memory” register M.
    MOV M B
– copy the data from register B into a memory location.
  Which memory location?
The memory location is identified by the contents of the HL register pair.
  The 16-bit contents of the HL register pair are treated as a 16-bit address and used to identify the memory location.

## Slide 7: Using the Other Register Pairs
There is also an instruction for moving data from memory to the accumulator without disturbing the contents of the H and L register.
  LDAX Rp (LoaD Accumulator eXtended)
    Copy the 8-bit contents of the memory location identified by the Rp register pair into the Accumulator.
    This instruction only uses the BC or DE pair.
    It does not accept the HL pair.

## Slide 8: Indirect Addressing Mode
Using data in memory directly (without loading first into a Microprocessor’s register) is called Indirect Addressing.
Indirect addressing uses the data in a register pair as a 16-bit address to identify the memory location being accessed.
  The HL register pair is always used in conjunction with the memory register “M”.
  The BC and DE register pairs can be used to load data into the Accumultor using indirect addressing.

## Slide 9: Arithmetic Operations
Addition (ADD, ADI):
  Any 8-bit number.
  The contents of a register.
  The contents of a memory location.
Can be added to the contents of the accumulator and the result is stored in the accumulator.
Subtraction (SUB, SUI):
  Any 8-bit number
  The contents of a register
  The contents of a memory location
Can be subtracted from the contents of the accumulator. The result is stored in the accumulator.

## Slide 10: Arithmetic Operations Related to Memory
These instructions perform an arithmetic operation using the contents of a memory location while they are still in memory.
  ADD M
    Add the contents of M to the Accumulator
  SUB M
    Sub the contents of M from the Accumulator
  INR M / DCR M
    Increment/decrement the contents of the memory location in place.
  All of these use the contents of the HL register pair to identify the memory location being used.

## Slide 11: Arithmetic Operations
Increment (INR) and Decrement (DCR):
  The 8-bit contents of any memory location or any register can be directly incremented or decremented by 1.
  No need to disturb the contents of the accumulator.

## Slide 12: Manipulating Addresses
Now that we have a 16-bit address in a register pair, how do we manipulate it?
It is possible to manipulate a 16-bit address stored in a register pair as one entity using some special instructions.
The register pair is incremented or decremented as one entity. No need to worry about a carry from the lower 8-bits to the upper. It is taken care of automatically.
INX Rp
DCX Rp
(Increment the 16-bit number in the register pair) (Decrement the 16-bit number in the register pair)

## Slide 13: Logic Operations
These instructions perform logic operations on the contents of the accumulator.
  ANA, ANI, ORA, ORI, XRA and XRI
    Source: Accumulator and
      An 8-bit number
      The contents of a register
      The contents of a memory location
    Destination: Accumulator
ANA ANI | R/M # | AND Accumulator With Reg/Mem AND Accumulator With an 8-bit number
ORA | R/M | OR Accumulator With Reg/Mem
ORI | # | OR Accumulator With an 8-bit number
XRA | R/M | XOR Accumulator With Reg/Mem
XRI | # | XOR Accumulator With an 8-bit number

## Slide 14: Logic Operations
Complement:
  1’s complement of the contents of the accumulator.
CMA No operand

## Slide 15: Additional Logic Operations
Rotate
Rotate the contents of the accumulator one position to the left or right.
RLC
RAL
RRC
RAR
Rotate the accumulator left.
Bit 7 goes to bit 0 AND the Carry flag.
Rotate the accumulator left through the carry. Bit 7 goes to the carry and carry goes to bit 0.
Rotate the accumulator right.
Bit 0 goes to bit 7 AND the Carry flag.
Rotate the accumulator right through the carry. Bit 0 goes to the carry and carry goes to bit 7.

## Slide 16: RLC vs. RLA
RLC
RAL
Accumulator
Carry Flag
7
6
5
4
3
2
1
0
Accumulator
Carry Flag
7
6
5
4
3
2
1
0

## Slide 17: Logical Operations
Compare
  Compare the contents of a register or memory location with the contents of the accumulator.
– CMP | R/M | Compare the contents of the register or memory location to the contents of the accumulator.
– CPI | # | Compare the 8-bit number to the contents of the accumulator.
The compare instruction sets the flags (Z, Cy, and S).
The compare is done using an internal subtraction that does not change the contents of the accumulator.
A – (R / M / #)

## Slide 18: Branch Operations
Two types:
  Unconditional branch.
    Go to a new location no matter what.
  Conditional branch.
    Go to a new location if the condition is true.

## Slide 19: Unconditional Branch
– JMP
Address
Jump to the address specified (Go to).
CALL Address
  Jump to the address specified but treat it as a subroutine.
RET
  Return from a subroutine.
– The addresses supplied to all branch operations must be 16-bits.

## Slide 20: Conditional Branch
Go to new location if a specified condition is met.
  JZ Address (Jump on Zero)
    Go to address specified if the Zero flag is set.
  JNZ Address (Jump on NOT Zero)
    Go to address specified if the Zero flag is not set.
  JC Address (Jump on Carry)
    Go to the address specified if the Carry flag is set.
  JNC Address (Jump on No Carry)
    Go to the address specified if the Carry flag is not set.
  JP Address (Jump on Plus)
    Go to the address specified if the Sign flag is not set
  JM Address (Jump on Minus)
    Go to the address specified if the Sign flag is set.

## Slide 21: Machine Control
HLT
  Stop executing the program.
NOP
  No operation
  Exactly as it says, do nothing.
  Usually used for delay or to replace instructions during debugging.

## Slide 22: Operand Types
There are different ways for specifying the operand:
  There may not be an operand (implied operand)
    CMA
  The operand may be an 8-bit number (immediate data)
    ADI 4FH
  The operand may be an internal register (register)
    SUB B
  The operand may be a 16-bit address (memory address)
    LDA 4000H

## Slide 23: Instruction Size
Depending on the operand type, the instruction may have different sizes. It will occupy a different number of memory bytes.
  Typically, all instructions occupy one byte only.
  The exception is any instruction that contains immediate data or a memory address.
    Instructions that include immediate data use two bytes.
      One for the opcode and the other for the 8-bit data.
    Instructions that include a memory address occupy three bytes.
      One for the opcode, and the other two for the 16-bit address.

## Slide 24: Instruction with Immediate Data
Operation: Load an 8-bit number into the accumulator.
  MVI A, 32
    Operation: MVI A
    Operand: The number 32
    Binary Code:
0011 1110 3E 1st byte.
0011 0010 32 byte.

## Slide 25: Instruction with a Memory Address
Operation: go to address 2085.
  Instruction: JMP 2085
    Opcode: JMP
    Operand: 2085
    Binary code:
1100 0011 C3 1st byte.
1000 0101 | 85 | 2nd byte
0010 0000 | 20 | 3rd byte

## Slide 26: Addressing Modes
The microprocessor has different ways of specifying the data for the instruction. These are called “addressing modes”.
The 8085 has four addressing modes:
Implied
Immediate
Direct
Indirect
CMA MVI B, 45
LDA 4000 LDAX B
Load the accumulator with the contents of the memory location whose address is stored in the register pair BC).

## Slide 27: Data Formats
In an 8-bit microprocessor, data can be represented in one of four formats:
  ASCII
  BCD
  Signed Integer
  Unsigned Integer.
It is important to recognize that the microprocessor deals with 0’s and 1’s.
  It deals with values as strings of bits.
  It is the job of the user to add a meaning to these strings.

## Slide 28: Data Formats
Assume the accumulator contains the following value: 0100 0001.
  There are four ways of reading this value:
    It is an unsigned integer expressed in binary, the equivalent decimal number would be 65.
    It is a number expressed in BCD (Binary Coded Decimal) format. That would make it, 41.
    It is an ASCII representation of a letter. That would make it the letter A.
    It is a string of 0’s and 1’s where the 0th and the 6th bits are set to 1 while all other bits are set to 0.
ASCII stands for American Standard Code for Information Interchange.