## Slide 1: Counters & Time Delays

## Slide 2: Counters
A loop counter is set up by loading a register with a certain value
Then using the DCR (to decrement) and INR (to increment) the contents of the register are updated.
A loop is set up with a conditional jump instruction that loops back or not depending on whether the count has reached the termination count.

## Slide 3: Counters
The operation of a loop counter can be described using the following flowchart.
Initialize
Update the count
Is this Final Count?
Body of loop
No
Yes

## Slide 4
Sample ALP for implementing a loop Using DCR instruction
MVI C, 15H
LOOP
DCR C JNZ LOOP

## Slide 5: Using a Register Pair as a Loop Counter
Using a single register, one can repeat a loop for a maximum count of 255 times.
It is possible to increase this count by using a register pair for the loop counter instead of the single register.
  A minor problem arises in how to test for the final count since DCX and INX do not modify the flags.
  However, if the loop is looking for when the count becomes zero, we can use a small trick by ORing the two registers in the pair and then checking the zero flag.

## Slide 6: Using a Register Pair as a Loop Counter
The following is an example of a loop set up with a register pair as the loop counter.
LXI B, 1000H
LOOP DCX B
MOV A, C
ORA B
JNZ LOOP

## Slide 7: Delays
It was earlier that each instruction passes through different combinations of Fetch, Memory Read, and Memory Write cycles.
Knowing the combinations of cycles, one can calculate how long such an instruction would require to complete.
The table in Appendix F of the book contains a column with the title B/M/T.
  B for Number of Bytes
  M for Number of Machine Cycles
  T for Number of T-State.

## Slide 8: Delays
Knowing how many T-States an instruction requires, and keeping in mind that a T-State is one clock cycle long, we can calculate the time using the following formula:
Delay = No. of T-States / Frequency
For example a “MVI” instruction uses 7 T-States. Therefore, if the Microprocessor is running at 2 MHz, the instruction would require 3.5 Seconds to complete.

## Slide 9: Delay loops
We can use a loop to produce a certain amount of time delay in a program.
The following is an example of a delay loop:
The first instruction initializes the loop counter and is executed only once requiring only 7 T-States.
The following two instructions form a loop that requires 14 T-States to execute and is repeated 255 times until C becomes 0.
MVI C, FFH LOOP DCR C
JNZ LOOP
7 T-States
4 T-States
10 T-States

## Slide 10: Delay Loops (Contd.)
We need to keep in mind though that in the last iteration of the loop, the JNZ instruction will fail and require only 7 T-States rather than the 10.
Therefore, we must deduct 3 T-States from the total delay to get an accurate delay calculation.
To calculate the delay, we use the following formula:
Tdelay = TO + TL
  Tdelay = total delay
  TO = delay outside the loop
  TL = delay of the loop
TO is the sum of all delays outside the loop.

## Slide 11: Delay Loops (Contd.)
Using these formulas, we can calculate the time delay for the previous example:
TO = 7 T-States
  Delay of the MVI instruction
TL = (14 X 255) - 3 = 3567 T-States
  14 T-States for the 2 instructions repeated 255 times (FF16 = 25510) reduced by the 3 T-States for the final JNZ.

## Slide 12: Using a Register Pair as a Loop Counter
Using a single register, one can repeat a loop for a maximum count of 255 times.
It is possible to increase this count by using a register pair for the loop counter instead of the single register.
  A minor problem arises in how to test for the final count since DCX and INX do not modify the flags.
  However, if the loop is looking for when the count becomes zero, we can use a small trick by ORing the two registers in the pair and then checking the zero flag.

## Slide 13: Using a Register Pair as a Loop Counter
The following is an example of a delay loop set up with a register pair as the loop counter.
LXI B, 1000H LOOP DCX B
MOV A, C ORA B JNZ LOOP
10 T-States
6 T-States
4 T-States
4 T-States
10 T-States

## Slide 14: Using a Register Pair as a Loop Counter
Using the same formula from before, we can calculate:
TO = 10 T-States
  The delay for the LXI instruction
TL = (24 X 4096) - 3 = 98301 T- States
  24 T-States for the 4 instructions in the loop repeated 4096 times (100016 = 409610) reduced by the 3 T- States for the JNZ in the last iteration.

## Slide 15: Nested Loops
Nested loops can be easily setup in Assembly language by using two registers for the two loop counters and updating the right register in the right loop.
– In the figure, the body of loop2 can be before or after loop1.
Initialize loop 1
Update the count1
Is this Final Count?
Body of loop 1
No
Yes
Initialize loop 2
Body of loop 2
Update the count 2
Is this Final Count?
No
Yes

## Slide 16: Nested Loops for Delay
Instead (or in conjunction with) Register Pairs, a nested loop structure can be used to increase the total delay produced.
 | MVI B, 10H | 7 T-States
LOOP2 | MVI C, FFH | 7 T-States
LOOP1 | DCR C | 4 T-States
 | JNZ LOOP1 | 10 T-States
 | DCR B | 4 T-States
 | JNZ LOOP2 | 10 T-States

## Slide 17: Delay Calculation of Nested Loops
The calculation remains the same except that it the formula must be applied recursively to each loop.
  Start with the inner loop, then plug that delay in the calculation of the outer loop.
Delay of inner loop
  TO1 = 7 T-States
    MVI C, FFH instruction
– TL1 = (255 X 14) - 3 = 3567 T-States
    14 T-States for the DCR C and JNZ instructions repeated 255 times (FF = 255 ) minus 3 for the final JNZ

## Slide 18: Delay Calculation of Nested Loops
Delay of outer loop
  TO2 = 7 T-States
    MVI B, 10H instruction
– TL1 = (16 X (14 + 3574)) - 3 = 57405 T-States
    14 T-States for the DCR B and JNZ instructions and 3574
T-States for loop1 repeated 16 times (1016 = 1610) minus 3 for the final JNZ.
– TDelay = 7 + 57405 = 57412 T-States
Total Delay
– TDelay = 57412 X 0.5 Sec = 28.706 mSec

## Slide 19: Increasing the delay
The delay can be further increased by using register pairs for each of the loop counters in the nested loops setup.
It can also be increased by adding dummy instructions (like NOP) in the body of the loop.