## Slide 1: Stack and Subroutines

## Slide 2: The Stack
The stack is an area of memory identified by the programmer for temporary storage of information.
The stack is a LIFO structure.
– Last In First Out.
The stack normally grows backwards into memory.
– In other words, the programmer defines the bottom of the stack and the stack grows up into reducing address range.
Memory
Bottom of the Stack
The Stack grows backwards into memory

## Slide 3: The Stack
Given that the stack grows backwards into memory, it is customary to place the bottom of the stack at the end of memory to keep it as far away from user programs as possible.
In the 8085, the stack is defined by setting the SP (Stack Pointer) register.
LXI SP, FFFFH
This sets the Stack Pointer to location FFFFH (end of memory for the 8085).

## Slide 4: Saving Information on the Stack
Information is saved on the stack by PUSHing it on.
  It is retrieved from the stack by POPing it off.
The 8085 provides two instructions: PUSH and POP for storing information on the stack and retrieving it back.
  Both PUSH and POP work with register pairs ONLY.

## Slide 5: The PUSH Instruction
PUSH B
  Decrement SP
  Copy the contents of register B to the memory location pointed to by SP
– Decrement SP
– Copy the co12ntenFt3s of reg C to the memory location pointed to by SP

## Slide 6: The POP Instruction
POP D
  Copy the contents of the memory location pointed to by the SP to register E
  Increment SP
– Copy the contents of the memory location
– Increment SP

## Slide 7: Operation of the Stack
During pushing, the stack operates in a “decrement then store” style.
  The stack pointer is decremented first, then the information is placed on the stack.
During poping, the stack operates in a “use then increment” style.
  The information is retrieved from the top of the the stack and then the pointer is incremented.
The SP pointer always points to “the top of the stack”.

## Slide 8: LIFO
The order of PUSHs and POPs must be opposite of each other in order to retrieve information back into its original location.
PUSH B
PUSH D
...
POP D
POP B

## Slide 9: The PSW Register Pair
The 8085 recognizes one additional register pair called the PSW (Program Status Word).
  This register pair is made up of the Accumulator and the Flags registers.
It is possible to push the PSW onto the stack, do whatever operations are needed, then POP it off of the stack.
  The result is that the contents of the Accumulator and the status of the Flags are returned to what they were before the operations were executed.

## Slide 10: Subroutines
A subroutine is a group of instructions that will be used repeatedly in different locations of the program.
  Rather than repeat the same instructions several times, they can be grouped into a subroutine that is called from the different locations.
In Assembly language, a subroutine can exist anywhere in the code.
  However, it is customary to place subroutines separately from the main program.

## Slide 11: Subroutines
The 8085 has two instructions for dealing with subroutines.
  The CALL instruction is used to redirect program execution to the subroutine.
  The RTE insutruction is used to return the execution to the calling routine.

## Slide 12: The RTE Instruction
RTE
  Retrieve the return address from the top of the stack
  Load the program counter with the return address
PC
FFFB FFFC FFFD FFFE FFFF
03
20
2 0 0 3
4014
4015
. . . RTE
SP

## Slide 13: Cautions
The CALL instruction places the return address at the two memory locations immediately before where the Stack Pointer is pointing.
  You must set the SP correctly BEFORE using the CALL instruction.
The RTE instruction takes the contents of the two memory locations at the top of the stack and uses these as the return address.
  Do not modify the stack pointer in a subroutine. You will loose the return address.