## Slide 1: 8051 Software Overview

## Slide 2: Overview
Addressing Mode
Instruction Set
Programming

## Slide 3: 8051 Addressing Modes
The CPU can access data in various ways, which are called addressing modes
  Immediate
  Register
  Direct
  Register indirect
  External Direct

## Slide 4: Immediate Addressing Mode
The source operand is a constant.
The immediate data must be preceded by the pound sign, “#”
Can load information into any registers, including 16-bit DPTR register
  DPTR can also be accessed as two 8-bit registers, the high byte DPH and low byte DPL

## Slide 5: Register Addressing Mode
Use registers to hold the data to be manipulated.
The source and destination registers must match in size.
  MOV DPTR,A will give an error
The movement of data between Rn registers is not allowed
  MOV R4,R7 is invalid

## Slide 6: Direct Addressing Mode
It is most often used the direct addressing mode to access RAM locations 30 – 7FH.
The entire 128 bytes of RAM can be accessed.
Contrast this with immediate addressing mode, there is no “#” sign in the operand.

## Slide 7: SFR Registers & their Addresses
MOV 0E0H,#55H ;is the same as
MOV A,#55H ;which means load 55H into A (A=55H)
MOV 0F0H,#25H ;is the same as
MOV B,#25H ;which means load 25H into B (B=25H)
MOV 0E0H,R2 ;is the same as
MOV A,R2 ;which means copy R2 into A
MOV 0F0H,R0 ;is the same as
MOV B,R0 ;which means copy R0 into B

## Slide 8: SFR Addresses ( 1 of 2 )

## Slide 9: SFR Addresses ( 2 of 2 )

## Slide 10: Example
Write a code send 55H to ports P1 and P2, using (a) their names and (b) their address.

## Slide 11: Example
Write a code send 55H to ports P1 and P2, using (a) their names and (b) their address.
Solution:
MOV A, #55H
MOV P1, A
MOV P2, A
MOV A, #55H
MOV 80H, A
MOV 0A0H, A

## Slide 12: Stack and Direct Addressing Mode
Show the code to push R5 and A onto the stack and then pop them into R2 and B, where B = A and R2 = R5.
Solution: ??????

## Slide 13: Stack and Direct Addressing Mode
Show the code to push R5 and A onto the stack and then pop them into R2 and B, where B = A and R2 = R5.
Solution:

## Slide 14: Register Indirect Addressing Mode
A register is used as a pointer to the data.
Only register R0 and R1 are used for this purpose.
R2 – R7 cannot be used to hold the address of an operand located in RAM.
When R0 and R1 hold the addresses of RAM locations, they must be preceded by the “@” sign.

## Slide 15: Register Indirect Addressing Mode
Write a program to copy the value 55H into RAM memory locations 40H to 41H using (a) direct addressing mode, (b) register indirect addressing mode without a loop, and (c) with a loop.
Solution????

## Slide 16: Register Indirect Addressing Mode
Write a program to copy the value 55H into RAM memory locations 40H to 41H using (a) direct addressing mode, (b) register indirect addressing mode without a loop, and (c) with a loop.
Solution for (a)

## Slide 17: Register Indirect Addressing Mode
Write a program to copy the value 55H into RAM memory locations 40H to 41H using (a) direct addressing mode, (b) register indirect addressing mode without a loop, and (c) with a loop.
Solution for (b)

## Slide 18: Register Indirect Addressing Mode
Write a program to copy the value 55H into RAM memory locations 40H to 41H using (a) direct addressing mode, (b) register indirect addressing mode without a loop, and (c) with a loop.
Solution for (c)

## Slide 19: Register Indirect Addressing Mode
The advantage is that it makes accessing data dynamic rather than static as in direct addressing mode.
Looping is not possible in direct addressing mode.
Write a program to clear 16 RAM locations starting at RAM address 60H.
Solution: ????

## Slide 20: Register Indirect Addressing Mode
The advantage is that it makes accessing data dynamic rather than static as in direct addressing mode.
Looping is not possible in direct addressing mode.
Write a program to clear 16 RAM locations starting at RAM address 60H.
Solution:

## Slide 21: External Direct
External Memory is accessed.
There are only two commands that use External Direct addressing mode:
  MOVX A, @DPTR MOVX @DPTR, A
DPTR must first be loaded with the address of external memory.

## Slide 22: Instruction Set
8051 instructions have 8-bit opcode
There are 256 possible instructions of which 255 are implemented.

## Slide 23: ASSEMBLER DIRECTIVES
The assembling directives give the directions to the CPU. The 8051 microcontroller consists of various kinds of assembly directives to give the direction to the control unit. The most useful directives are 8051 programming, such as:
ORG
DB
EQU
END

## Slide 25: ORG (Origin)
This directive indicates the start of the program.
This is used to set the register address during assembly.
For example; ORG 0000h tells the compiler all subsequent code starting at address 0000h

## Slide 28: End
END:The END directive is used to indicate the end of the program.
Syntax:
reg equ,09h
—————– —————– MOV reg,#2h END

## Slide 31: MOV Instruction
MOV destination, source ; copy source to destination.
MOV A,#55H ;load value 55H into reg. A MOV R0,A ;copy contents of A into R0 ;(now A=R0=55H) MOV R1,A ;copy contents of A into R1 ;(now A=R0=R1=55H) MOV R2,A ;copy contents of A into R2 ;(now A=R0=R1=R2=55H) MOV R3,#95H ;load value 95H into R3 ;(now R3=95H) MOV A,R3 ;copy contents of R3 into A ;now A=R3=95H

## Slide 32: ADD Instruction
ADD A, source ;ADD the source operand to the accumulator
MOV A, #25H ;load 25H into A MOV R2,#34H ;load 34H into R2 ADD A,R2 ;add R2 to accumulator ;(A = A + R2)

## Slide 33: Structure of Assembly Language
ORG 0H ;start (origin) at location 0 MOV R5,#25H ;load 25H into R5 MOV R7,#34H ;load 34H into R7 MOV A,#0 ;load 0 into A ADD A,R5 ;add contents of R5 to A ;now A = A + R5 ADD A,R7 ;add contents of R7 to A ;now A = A + R7 ADD A,#12H ;add to A value 12H ;now A = A + 12H
HERE: SJMP HERE ;stay in this loop END ;end of asm source file

## Slide 34: Data Types & Directives
  ORG 500H
  DATA1: DB 28 ;DECIMAL (1C in Hex)
  DATA2: DB 00110101B ;BINARY (35 in Hex)
  DATA3: DB 39H ;HEX
  ORG 510H
  DATA4: DB “2591” ; ASCII NUMBERS
  ORG 518H
  DATA6: DB “My name is Joe” ;ASCII CHARACTERS

## Slide 35: ADD Instruction and PSW
Show the status of the CY, AC and P flags after the addition of 38H and 2FH in the following instructions.
MOV A,#38H
ADD A, #2FH ; after the addition A = 67H, CY = 0
Solution:????

## Slide 36: ADD Instruction and PSW
Show the status of the CY, AC and P flags after the addition of 38H and 2FH in the following instructions.
MOV A,#38H
ADD A, #2FH ; after the addition A = 67H, CY = 0
Solution:

## Slide 37: ADD Instruction and PSW
Show the status of the CY, AC and P flags after the addition of 9CH and 64H in the following instructions.
MOV A,#9CH
ADD A, #64H ; after the addition A = 00H, CY = 1
Solution:????

## Slide 38: ADD Instruction and PSW
Show the status of the CY, AC and P flags after the addition of 9CH and 64H in the following instructions.
MOV A,#9CH
ADD A, #64H ; after the addition A = 00H, CY = 1
Solution:

## Slide 39: Multiplication of Unsigned Numbers
MUL AB ; A x B, place 16-bit result in B and A
MOV A,#25H ;load 25H to reg. A
MOV B,#65H ;load 65H in reg. B
MUL AB ;25H * 65H = E99 where B = 0EH and A = 99H

## Slide 40: Division of Unsigned Numbers
DIV AB ; divide A by B
MOV A,#95H ;load 95 into A
MOV B,#10H ;load 10 into B
DIV AB ;now A = 09 (quotient) and B = 05 (remainder)

## Slide 41: Checking an input bit
JNB (jump if no bit) ; JB (jump if bit = 1)
Assume that bit P2.3 is an input and represents the condition of an oven. If it goes high, it means that the oven is hot. Monitor the bit continuously. Whenever it goes high, send a high-to-low pulse to port P1.5 to turn on a buzzer.
Solution????

## Slide 42: Checking an input bit
JNB (jump if no bit) ; JB (jump if bit = 1)
Assume that bit P2.3 is an input and represents the condition of an oven. If it goes high, it means that the oven is hot. Monitor the bit continuously. Whenever it goes high, send a high-to-low pulse to port P1.5 to turn on a buzzer.
Solution:
HERE: JNB P2.3, HERE ; Keep monitoring for high
SETB P1.5 ; Set bit P1.5 = 1
CLR P1.5 ; make high-to-low

## Slide 43: Switch Register Banks
Solution????

## Slide 44: Switch Register Banks
Solution:

## Slide 45: Pushing onto Stack
Solution????

## Slide 46: Pushing onto Stack
Solution:

## Slide 47: Popping from Stack
Solution????

## Slide 48: Popping from Stack
Solution:

## Slide 49: Looping
Write a program to
  Clear ACC, then
  Add 3 to the accumulator ten times.

## Slide 50: Looping
Write a program to
  Clear ACC, then
  Add 3 to the accumulator ten times.

## Slide 51: Loop inside a Loop (Nested Loop)
Write a program to (a) load the accumulator with the values 55H and (b) complement the ACC 700 times.
Solution??

## Slide 52: Loop inside a Loop (Nested Loop)
Write a program to (a) load the accumulator with the values 55H and (b) complement the ACC 700 times.
Solution:

## Slide 53: 8051 Conditional Jump Instructions

## Slide 55: Conditional Jump Example
Write a program to determine if R5 contains the value 0. If so, out 55H in it.
Solution??

## Slide 56: Conditional Jump Example
Write a program to determine if R5 contains the value 0. If so, out 55H in it.
Solution
MOV A, R5 ; Copy r5 to a
JNZ NEXT ; Jump If A Is Not Zero
NEXT: …

## Slide 57: Conditional Jump Example
Find the sum of the values 79H, F5H, and E2H. Put the sum in registers R0 (low byte) and R5 (high byte)
Solution???

## Slide 58: Conditional Jump Example
Find the sum of the values 79H, F5H, and E2H. Put the sum in registers R0 (low byte) and R5 (high byte)
Solution:

## Slide 59: Unconditional Jump Instructions
All conditional jumps are short jumps
  Target address within -128 to +127 of PC
LJMP (long jump): 3-byte instruction
  2-byte target address: 0000 to FFFFH
  Original 8051 has only 4KB on-chip ROM
SJMP (short jump): 2-byte instruction
  1-byte relative address: -128 to +127

## Slide 60: Call Instructions
LCALL (long call): 3-byte instruction
  2-byte address
  Target address within 64K-byte range
ACALL (absolute call): 2-byte instruction
  11-bit address
  Target address within 2K-byte range